## Slide 1: High Level applications development status
H. Guler for the ThomX commissioning group

## Slide 2: Motivations/Goals
General machine startup strategy
General machine control strategy
Provide tools for Linac commissioning (TL-LE)
  On top of Tango Tools
  Give an alternative to basic Atkpanels
    Combined information
    Modified information (fitting, calculations, etc )
  Strategy for measurements types
  Strategy for data taking
  Strategy for publications on eLog (visible from outside LAL)
  Interlock management
    General pane (+ Tango tools)

## Slide 3: Some basic rules
Knowledge / basic understanding of TANGO (Training at control room)
Interfaces to be implemented by using MATLAB (MML) and / or directly using Python (Taurus, …)
High level interfaces design should be done by machine experts and could evolve
  Periods of training and development is necessary
  Easy installation, versioning, and user manuals are needed
General single common scripts for raw signal analysis :
  Beam charge extraction (from Wavecatcher)
  YAG : Spot analysis tool (extract size, position, … )
  BPMs …
Physical variables (Calibrations, Twiss parameters, …) coming from calculation should be included in Tango DS
  No differences for same variable should appear in different IHM
Single programing language is not mandatory (MATLAB, Python)
  Matlab : Tango-binding
  Python : PyTango

## Slide 4
________________TANGO _______________
Hardware 1
Hardware 6
Hardware 2
Hardware 3
Hardware 4
Hardware 5
Data : access data, contrôle timouts, save data etc :
PyTango / MatLab-Tango binding
Interfaces : IHM (contrôle equipment, show data, …)
Python (Taurus, PyQt, ..) – MatLab (MML) – Labview - Java
Saved data
Write to eLog
Manage machine alarms

## Slide 5: From simulation to first tests
Linux platform (tango-util2) deployed with TANGO9 and simulation Ds
  Python software could generate sim-Ds from Ds
    Magnets + Cycling Ds
    Libera, RedPytaya
During commissioning : Development could be done on sim-Ds
  Simulator-DS functionality still to be understood
Repository process will be used
  Git / GitLab
  Keep development history : nothing lost / improve efficiency
  Cross check : each modification should be approved by other developer
Notes: Utills pour les tests

## Slide 6: Linac commisioning needs
IHM to startup all the Linac sub-systems
  General startup IHM
IHM to monitor the machine status
  Simple general status manager
  Quickly see equipment with problems (Green vs Red color in IHM)
tools to control the beam and to tune the machine
  Algorithms which combines diagnostics and accelerator parameters
data saving strategy
  All data from different measurements
  Quick analysis tools / environment  improve decision quality during shifts
  Offline analysis  easily retrieve and analyze data
easy reporting
  Elog : tools to automatically (or not) save needed data

## Slide 7: Linac commissioning : basic objects
Tasks | Details | Device Server | Measured quantity | Data
Magnets cycling |  | Magnet and Cycling |  | 
Energy steerer |  |  |  | 
Beam size and position | Screen + barycenter + size | Lima |  | Image Sx,Sy,X,Y
Bunch charge screen | Screen calibration in charge | Lima | Calibration coefficient in DS | Image
Bunch charge ICT |  | Wavecatcher | Waveform | Integral(WF)
Laser E, size Virtual Cathod | UV Camera | Lima |  | E, Sx,Sy,X,Y
Laser pulse length | Streak |  |  | Image
Faraday Cup |  | Wavecatcher | Waveform | 
BPM |  | Libera |  | 

## Slide 8: Linac commissioning : machine tuning
Use of scans / measurements :
  Algorithms to be called inside IHMs
    Examples :
      Charge vs Phase
      Charge vs solenoid current
    Dedicated IHM for Diagnostics should contain :
      Measurement selection
        Which includes list of variables that should be saved
        Includes measurement parameters to be set to the algorithm
        Button to send analysis to eLog  Template to be prepared
        Prepare tango-device with list of variables to be saved (calibrations, …)

## Slide 9: Linac commissioning : Equipment interfaces
IHM | Language | Status
Linac Laser | Python (Taurus) | 90%
Modulator | Java | 90%
RF GUN | Python (Taurus) | 90%
RF Section | Python (Taurus) | 90%
Vacuum | LabView | 90%
PowerSupply | Python (Taurus) | 90%
Icepap supervision | LabView | 90%
LASER
Magnets
powersupply
RF-Section
RF-GUN

## Slide 10: Linac commissioning : Equipment interfaces
IHM | Language | Status
Linac Laser | Python (Taurus) | 90%
Modulator | Java | 90%
RF GUN | Python (Taurus) | 90%
RF Section | Python (Taurus) | 90%
Vacuum | LabView | 90%
PowerSupply | Python (Taurus) | 90%
Icepap supervision | LabView | 90%
Vacuum IHM
ICEPAP Wheel
supervision

## Slide 11: Linac commissioning : Equipment interfaces
IHM | Language | Status | Remark
Synchronizations | Python (Taurus) | On going | 
Diagnostics |  | On going | To be done with commissioning group
General startup | Python (Taurus) | On going | To be done with commissioning group
General Status | Python (Taurus) | On going | To be done with commissioning group
Alarm status |  | On going | To be done with Interlock group
Machine synoptic |  | On going | To be done with commissioning group

## Slide 12: Need for trend plots : easy to compute and very useful

## Slide 13: Interfaces needed for beam tuning for single pass (Linac-TL-EL)
During the Linac + TL + EL commissioning
  To help the beam tuning
    Useful for beam alignment
    Follow trends for ICT, BPMs
      For example Trend of the beam charge / position
Example of interface @CLEAR
  Choose screen
  Measure beam spot size, position
    Plots trends
  Get beam charge / position at different locations
    Plot trends
Example of interface used at PHIL
Taurus provide Taurustrend, taurusplot, taurusform …

## Slide 14: Trend plots for vacuum
During RF conditioning for RF-Gun or Linac Section.
Very useful for conditioning

## Slide 15: Scan measurements : To be adapted for ThomX

## Slide 16: Example of Scan interfaces to be included in MML Charge phase scan (from CLEAR)
Script to adapt for ThomX (could be done in MML or Taurus )

## Slide 17: Example scan for energie steerer

## Slide 18: Example of solenoide scan

## Slide 19: Interface with RF-Signals
Could be very useful to understand the Timing status
Need to keep the possibility to access the analog signals (scope)

## Slide 20: Interfaces roadmap : commisioning
Interface for Linac commissioning are essential for commissioning
  Equipment startup
  Monitor equipment
Tune the machine :
  Strategy for the data
  Set of Algorithms and use of dedicated tango variable
Collaborative future development in the ThomX control room
By training and working together IHM would change, adapt to our usage