## Slide 1: Perspectives on the route to a multi-TeV muon collider

## Slide 2: Contents
Ambition
Muon accelerators for particle physics
Muon collider
nuSTORM
To realise the ambition

## Slide 3: Ambition
Perspectives on the route to a multi-TeV muon collider

## Slide 4: Outstanding questions …
… for the accelerator-based programme:
  My take on part of P.Hernanez’ excellent introduction to ESPPU

## Slide 5: The Higgs as window on new physics
mHiggs= 125.09(24) GeV
  Standard Model: predictive & verified at this level of precision

## Slide 6: The Higgs as window on new physics
SM within uncertainty
  Motivates Higgs factory to reduce substantially
    Statistical and systematic uncertainties

## Slide 7: Neutrinos as window on origin of flavour
Related to physics at very high energy scale
  Motivates high-precision neutrino programme
    Large event samples and low systematic uncertainties
PMNS

## Slide 8: Energy frontier to illuminate limit of SM
Measurement at highest possible energy
  Experimental motivation clear!
    Theorists motivated by ‘meta-stability’ of SM

## Slide 9: And so, the ambition
Our ambition is to make measurements:
  Of the properties of the Higgs
    With the highest possible precision
  Of the properties of the neutrino
    With the highest possible precision
  Of the properties of matter
    At the highest possible energies
What is the role of muon beams?

## Slide 10: Muon accelerators for Particle Physics
Perspectives on the route to a multi-TeV muon collider

## Slide 11: Basis of potential
Muon mass:
  200 me ~ mm ~ 0.1 mp
Muon decay:
  ne, nm
  Precisely known energy spectrum
Energy frontier:
  No brem-/beam-sstrahlung
    Rate  m-4 [5  10-10 cf e]
  Enhanced coupling to Higgs
    Production rate  m2 [5  104 cf e+e-]
  Efficient acceleration
    Favourable rigidity
Physics of flavour:
  Precision neutrino physics
  Sensitive cLFV searches

## Slide 12: Line shape
Standard Model Higgs:
  M = 125 GeV; G=4.5 MeV
    Exquisite resolution
      R < 0.003%
“Two-state” Higgs:
  Deviation from SM line shape
  Resolve states
    Exquisite resolution!
B.Autin, A.Blondel, J.Ellis;
CERN 99-02, 1999
M.Greco,T.Han,Z.Liu

## Slide 13: Couplings/branching ratios
Standard Model Higgs
  Accurate threshold measurement
  Exploiting accurate knowledge of (narrow) energy spectrum
Beyond SM Higgs
  Exploit narrow energy spectrum to search for :
    Narrow resonances
    Unexpected thresholds
mbb > 100 GeV
M.Greco,T.Han,Z.Liu
arXiv:1306.2609

## Slide 14: The Standard Model and beyond
Energy frontier: big advantage over pp because fundamental fermion
Future study of the Higgs:
  Line width; establish single resonance (?) in s-channel with m+m-
  Couplings; requires > 1 TeV for complete, precise study

## Slide 15: Resurgence of interest: Pastrone Panel

## Slide 17: Neutrino Factory: sensitivity & precision
Unique:
  Large, high-energy νe (νe) flux
    Muon-beam cooling
  Favourable rigidity:
    Optimise E for given L

## Slide 18: Muon collider
Perspectives on the route to a multi-TeV muon collider

## Slide 19: Collider Parameter Examples
From the MAP collaboration: Proton source

## Slide 20: Source
The MERIT Experiment at the CERN PS
  Demonstrated a 20m/s liquid Hg jet injected into a 15 T solenoid and hit with a 115 KJ/pulse beam!
  Jets could operate with beam powers up to 8 MW with a repetition rate of 70 Hz
Hg jet in a 15 T solenoid: measured disruption length ~28 cm

## Slide 21: Cooling: the emittance path
Y
Transverse Emittance (microns)
Longitudinal Emittance (mm)
Bunch
Merge
For acceleration
to Higgs Factory
For acceleration to multi-TeV collider
Final
Cooling
post-merge 6D Cooling
For acceleration to NuMAX (325MHz injector acceptance 3mm,24mm)
Initial Cooling
Target
Phase
Rotator
Front End



pre-merge 6D Cooling (original design)
Exit Front End
(15mm,45mm)
Initial
(X)
Initial
(Y)
VCC &
Hybrid
HCC
Final
Specification Achieved (simulations)

## Slide 22: Muon Ionization Cooling Experiment

## Slide 23: The principle of ionization cooling
Competition between:
  dE/dx [cooling]
  MCS [heating]
Optimum:
  Low Z, large X0
  Tight focus
  H2 gives best performance

## Slide 25: Liquid-hydrogen absorber
Online reconstruction:
Mean momentum lost by muons as they pass through the liquid-hydrogen absorber.
The data were recorded while the absorber was filling.

## Slide 26: Emittance and amplitude
Emittance:
  Evaluated from RMS beam ellipse
Amplitude:
  Distance from core of beam
Mean amplitude ~ RMS emittance

## Slide 27: Effect of lithium-hydride absorber
Simulation in good agreement with data
  Example:
    eT = 6 mm
    P = 140 MeV/c
    Notation: P-eT = 6-140
Upstream
Downstream
px
px
py
py

## Slide 28: Core-density change across absorber
Core-density:
  Increases with LiH and LH2 absorbers
  Consistent with ‘no change’ for no absorber
Ionization-cooling signal
Ramp = ratio of cumulative density downstream to upstream
Preparing submission to nature.

## Slide 29: Other Tests
6D Ionization Cooling Designs
  Designs in hand that meet performance targets in simulations with stochastic effects
  Ready to move to engineering design and prototyping
  Able to reach target performance with Nb3Sn conductors (NO HTS)
RF operation in magnetic field (MTA program)
  Gas-filled cavity solution successful and performance extrapolates to the requirements of the NF and MC
  Vacuum cavity performance now consistent with models
  MICE Test Cavity significantly exceeds specified operating requirements in magnetic field
Final Cooling Designs
  Baseline design meets Higgs Factory specification and performs within factor of 2.2× of required transverse emittance for high energy MC (while keeping magnets within parameters to be demonstrated within the next year at NHMFL).
  Alternative options under study
Mark Palmer
MuCool: >50MV/m in 5 T field
NHFML
32 T solenoid with low-temperature HTS
FNAL
Breakthrough in HTS cables
FNAL
12 T/s HTS
0.6 T max
29

## Slide 30: Test Facility Example
Carlo Rubbia: The experimental realization of the presently described μ+μ- Ring Collider may
represent the most attractive addition of the future programs on the Standard Model to
further elucidate the physics of the Ho, requiring however a substantial amount of prior
R&D developments, which must be experimentally confirmed by the help of the Initial
Muon Cooling Experiment(al) program.
6D cooling experiment; example
Use 100 ns ESS pre-pulse with 3x1011 protons
Yields 3x107 μ- and 6x107 μ+ around 250 MeV

## Slide 31: Potential Approaches
Various options considered:
Recirculating linacs
Fast acceleration but typically only a few passages through RF, hence high RF cost
FFAGs
Static magnets, but only limited increase in energy possible
Rapid cycling synchrotron (RCS)
Potentially larger acceleration range at affordable cost
Could use combination of static superconducting and ramping normal-conducting magnets
But have to deal with energy in fast pulsing magnets

## Slide 32: Collider Ring
High field dipoles to minimise collider ring size and maximise luminosity
Minimise distances with no bending
Decaying muons impact accelerator components, detector and public
The latter becomes much worse with energy
Radiation to public in case LHC tunnel use
Might be best to use LHC tunnel to house muon accelerator and have dedicated new collider tunnel
Proposal to combine last accelerator ring and collider ring (Neuffer/Shiltsev) might reduce cost but creates many specific challenges
Strong focusing at IP to maximise luminosity
Becomes harder with increasing energy

## Slide 33: The LEMMA Scheme
Muon beams produced with low emittance with positron beam
(40 nm vs. 25 μm in proton scheme)
  No cooling required, use lower muon current
Positron beam:
  45 GeV, 3x1011 particles every 200 ns
  Passes through target and produces muon pairs
Muon bunches circulation O(2000) times muon accumulation (4.5x107)
Every 0.5 ms, the muon bunches are extracted and accelerated

## Slide 34: Key Issues
Small efficiency of converting positrons to muon pairs:
  Muon pair production small fraction of overall cross section (O(10-5))
  Most positrons lost with no muon produced
  Have to produce many positrons (difficult)
  O(100MW) synchrotron radiation
  High heat load and stress in target (also difficult)
The multiple scattering of the muons in the target:
  Theoretical best emittance of 600 nm (40nm assumed)
    Reduction of luminosity by factor 15
Small bunches to be accelerated and merged:
  No design for the merger yet
  Combination factor proportional to beam energy

## Slide 35: Ongoing LEMMA Effort
Address issues identified:
  Large emittance from target
    Use sequence of thin targets
  Combining bunches at high energy
    Producing bunches in pulses fashion
  Positron ring challenge
    Larger ring
  Positron production
    Improved concepts
  Did not yet reach competitive performance
    Work is ongoing

## Slide 36: nuSTORM
Perspectives on the route to a multi-TeV muon collider

## Slide 37: Neutrinos from stored muons
Scientific objectives:
  %-level (νeN)cross sections
    Double differential
  Sterile neutrino search
    Beyond Fermilab SBN
  Muon-accelerator test-bed
    E.g. 6D cooling experiment
Precise neutrino flux:
  Normalisation: < 1%
  Energy (and flavour) precise
p ⇢ m injection pass:
  “Flash” of muon neutrinos

## Slide 38: Neutrino flux
νμ flash:
  Pion: 6.3 × 1016 m-2 at 50m
  Kaon: 3.8 × 1014 m-2 at 50m
    Well separated from pion neutrinos
νe and νμ from muon decay:
  ~10 times as many νe as, e.g. J-PARC beam
  Flavour composition, energy spectrum
    Use for energy calibration
10.1146/annurev-nucl-102014-021930

## Slide 39: Sterile neutrino search @ FNAL
Adey et al., PRD 89 (2014) 071301

## Slide 40: To understand the nucleon and the nucleus
Neutrino unique probe: weak and chiral:
  Sensitive to flavour/isospin and 100% polarised
How could neutrino scattering help?
  Development of understanding of nucleus/nucleon (e.g.):
    Multi-nucleon correlations
    Precise determination of:
      Model parameters or, better,
      Theoretical (ab initio) description
Precise nN scattering measurements to:
  Constrain models of nucleus/nucleon:
    Exploiting isospin dependence, chirality, …
Benefit of nuSTORM:
  Precise flux and energy distribution

## Slide 41: Search for CPiV in lbl oscillations
Seek to measure asymmetry:
  P(nm ➤ ne) – P(nm ➤ ne)
Event rates convolution of:
  Flux, cross sections, detector mass, efficiency, E-scale
    Measurements at %-level required
  Theoretical description:
    Initial state momentum, nuclear excitations, final-state effects
Lack of knowledge of cross-sections leads to:
  Systematic uncertainties; and
  Biases; pernicious if n and n differ

## Slide 42: Systematic uncertainty and/or bias
Event mis-classification
Energy scale mis-calibration
Missing energy (neutrons)
Phys.Rev. D89 (2014) no.7, 073015; Coloma et al
Phys.Rev. D92 (2015) no.9, 091301; Ankowski et al
Uncertainty (cross section and ratio)

## Slide 43: Specification: energy range
Guidance from:
  Models:
    Region of overlap 0.5—8 GeV
  DUNE/Hyper-K far detector spectra:
    0.3—6 GeV
Cross sections depend on:
  Q2 and W:
    Assume (or specify) a detector capable of:
      Measuring exclusive final states
      Reconstructing Q2 and W
    → Em < 6 GeV
So, stored muon energy range:
DUNE
Hyper-K
1 < Em < 6 GeV

## Slide 44: nuSTORM for nN scattering @ CERN — parameters
New specification!
  Design update:
    1 < Em < 6 GeV
  Challenge for accelerator design!
  Benefit:
    Calibration via energy spectrum
    Statistical ‘mono-energetic beam’
SPS requirements table

## Slide 45: Overview
Extraction from SPS through existing tunnel
Siting of storage ring:
  Allows measurements to be made ‘on or off axis’
  Preserves sterile-neutrino search option

## Slide 46: Extraction and p-beam transport to target
Fast extraction at 100 GeV:
  CNGS-like scheme adopted;
    Apertures defined by horizontal and vertical septa reasonable
    Pulse structure (2 x 10.5 ms pulses) requires kicker upgrade
Beam transport to target:
  Extraction into TT60:
    Branch from HiRadMat beam line at 230 m (TT61)
  Require to match elevation and slope
  New tunnel at junction cavern after 290 m
  585 m transport to target

## Slide 47: Target and capture
FNAL scheme adopted:
  Low-Z target in magnetic horn
  Pair of quadrupoles collect particles horn focused
  Target and initial focusing contained in inert helium atmosphere
Graphite target, based on CNGS experience:
  Radiation-cooled graphite target embedded in water-cooled vessel
Containment and transport of pion beam with a 10% momentum spread:
  Base on scheme used successfully for AD in PS complex
Target complex design:
  Exploit extensive work done for CENF

## Slide 48: Storage ring
New design for decay ring:
  Central momentum between 1 GeV/c and 6 GeV/c;
  Momentum acceptance of up to ±16%
Hybrid FODO/FFA concept developed:
  Maintain large momentum and transverse dynamic acceptance simultaneously
  FODO optics used in the production straight
  Zero-chromaticity FFA cells used in arcs and return straight
Hybrid ring properties:
  Zero dispersion in the quadrupole injection/production straight; and
  Zero chromaticity in the arcs and return straight
    Limits overall chromaticity of ring.
Magnets:
  Superconducting combined-function magnets (B up to 2.6 T) in arcs
  Warm combined-function magnets used in return straight
  Large-aperture warm quadrupoles used in production straight
  Mean betatron functions in production and return straights large:
    Minimise betatron oscillations to minimise spread of the neutrino beam

## Slide 49: nuSTORM feasibility
Goal of PBC nuSTORM study:
  “A credible proposal for siting at CERN …”
achieved.
Challenges:
  Muon decay ring:
    FFA concept though feasible
    Require magnet development to allow production at a reasonable cost
  Detailed evaluation of:
    Proton-beam extraction, target and target complex
    Civil engineering studies and radiological implications
“ … the SPS can provide the beam and offers a credible fast extraction location allowing the beam to be directed towards a green field site at a suitable distance from existing infrastructure. Initial civil engineering sketches have established a potential footprint and the geology is amenable to an installation at an appropriate depth.”

## Slide 50: To realise the ambition
Perspectives on the route to a multi-TeV muon collider

## Slide 51: Options

## Slide 52: Timescales are long

## Slide 53: Muon collider

## Slide 54: Neutrinos

## Slide 55: Conclusions
Muon accelerators have the potential to:
  Contribute to the study of the Higgs boson
  Deliver multi-TeV lepton-antilepton collisions
    Bringing forward the exploration of the very highest energies
  Revolutionise the study of the neutrino
Energy-frontier R&D programme should therefore:
  Include muon collider R&D:
    A new test facility is an essential part of this effort
      Synergy with front-rank particle-physics should be exploited
nuSTORM:
  A front-rank neutrino facility based on stored muon beams
  A demonstrator for muon beams for particle physics
  Capable of serving the 6D-cooling demonstration crucial for muon collider