## Slide 1: Study of a 5-Cell Elliptical Superconducting Cavity for a Multi-turn Energy Recovery Linac
Carmelo Barbagallo, Patricia Duchesne, Ningyuan Hu, Guillaume Olry, Walid Kaabi, Fabian Zomer
Laboratoire de Physique des 2 Infinis Irène Joliot-Curie (IJCLab) - Accelerator Physics group – RF section
Université Paris-Saclay, Orsay, France
Journées Accélérateurs 2021 de la SFP, 13 October 2021 – 15 October 2021, Roscoff (France)
Acknowledgments: Dr. Shahnam Gorgi Zadeh, Universität Rostock, Fakultät für Informatik und Elektrotechnik

## Slide 2: PERLE and 5-cell SRF cavity
  PERLE (Powerful Energy Recovery Linac for Experiments): multi-turn ERL (Energy Recovery Linac) based on Superconducting RF (SRF) technology to be studied and later host at Orsay (France).
PERLE CDR, 2018 [1]
7 MeV
Injector
487 MeV
e--beam
80 MeV
80 MeV
ARC 1 = 87 MeV
ARC 2 = 167 MeV
ARC 3 = 247 MeV
ARC 4 = 327 MeV
ARC 5 = 407 MeV
ARC 6 = 487 MeV
LINAC 2 (80 MeV)
LINAC 1 (80 MeV)
Four 5-cell 801.58 MHz elliptical Nb cavities
Target Parameter [2] | Unit | Value
Injection energy | MeV | 7
Electron beam energy | MeV | 500
Normalized Emittance ϒεx,y | mm·mrad | 6
Average beam current | mA | 20
Bunch charge | pC | 500
Bunch length | mm | 3
Bunch spacing | ns | 25
RF frequency | MHz | 801.58
Duty factor | CW (Continuous Wave) | 
  The first 801.58 MHz 5-cell elliptical Nb cavity has already been fabricated at JLab on October 2017 [2]
  HOM-damping for ERLs is a challenge due to the presence of many turns (multi-bunch beam instabilities)
  Aim of the numerical study (CST Studio Suite®): 1) Identification of HOMs, 2) Analysis of the transmission curves of HOM couplers, 3) HOM-damping schemes
The first Nb 801.58 MHz 5-cell elliptical cavity fabricated at JLab [3].
Cavity Parameters | JLab Cavity
Frequency [MHz] | 801.58
Temperature [K] | 2.0
Cavity active length [mm] | 917.911
R/Q [Ω] | 524.25
Geometry Factor (G) [Ω] | 274.505
(mid-cell) [] | 4.62
(mid-cell) [-] | 2.38
Iris radius [mm] | 65
Beam Pipe radius [mm] | 65
Mid-cell equator diameter [mm] | 328
End-cell equator diameter [mm] | 328
Wall angle [degree] | 0
Cutoff TE11 [GHz] | 1.35
Cutoff TM01 [GHz] | 1.77
Cavity Parameters | JLab Cavity
Frequency [MHz] | 801.58
Temperature [K] | 2.0
Cavity active length [mm] | 917.911
R/Q [Ω] | 524.25
Geometry Factor (G) [Ω] | 274.505
 | 4.62
 | 2.38
Iris radius [mm] | 65
Beam Pipe radius [mm] | 65
Mid-cell equator diameter [mm] | 328
End-cell equator diameter [mm] | 328
Wall angle [degree] | 0
Cutoff TE11 [GHz] | 1.35
Cutoff TM01 [GHz] | 1.77

## Slide 3: HOMs: consequences and damping mechanisms
  HOMs (Higher Order Modes) are parasitic excited eigenmodes in a resonant accelerating RF cavity, other than and with frequency greater than the operational mode (FM = Fundamental Mode) [4].
  Why are HOMs dangerous for beam dynamics?
  Monopole HOMs:
    can lead to timing/phase errors and energy spread
    contribute to extra dynamic heat losses in cavity walls
  Dipole HOMs:
    can deflect the beam from its reference orbit: instable beam motion, transverse emittance growth, beam loss
TM011 mode (Monopole HOM) – f =1374.73 MHz
TE111 mode (Dipole HOM) – f =933.53 MHz
TM01-π mode (FM) – f =801.58 MHz
  How can we damp HOMs in SRF cavities?
  Coaxial HOM coupler on beam tubes
    Hook-type LHC coupler
    Probe-type LHC coupler
    DQW HOM coupler
  Waveguide dampers on beam tubes
  Absorbers in cavity-interconnecting beam tubes
  Coupling through Fundamental Power Coupler
  DQW HOM Coupler

## Slide 4: HOM numerical simulations: 3D-Eigenmode and Wakefield
  The eigenmodes of a resonator in a non-excited source-free and lossless medium are computed by solving the Helmholtz equations:
Helmholtz equations
Boundary conditions
  and
  on
  and
  on
Assumption: PEC (Perfect Electric Conductor) on conducting walls (Nb) and interior domain of vacuum
  Cavity-beam interaction: wakefields in time domain or impedances in frequency domain. The long-range wakefield commonly corresponds to the high impedance peaks and can lead to coupled-bunch instability issues [4].
q1 = excitation bunch
q2 = test charge
w(r,s) = wake potential = change of momentum on q2
The energy left behind q1 is called wakefield.
Wakefield in an elliptical cavity [6].
Longitudinal impedance [Ω]
Transverse impedance [Ω/m]
Transverse shunt impedance [Ω/m]
Longitudinal shunt impedance [Ω]
Eigenmode simulations
Wakefield simulations

## Slide 5: Identification of dangerous HOMs – HOM coupler transmission
  TM monopole modes (like TM010, TM011, TM020, T012)
  E-field component along cavity axis
  Trapped mode can interact with the subsequent bunch
  TM dipole modes (like TM110, TM111, TM120)
  Strong longitudinal E-field component off axis
  Possible deflection and subsequent beam resonant effect
  TE dipole modes (like TE111, TE112)
  Theoretically no longitudinal E-field component on and off axis (possible deflection)
  TM01-TEM transmission
  The notch effect is tuned to 801.58 MHz for monopole coupling.
  Couplers optimization needed to deliver a higher value of transmission.
  TE11-TEM transmission
  Hook coupler: higher transmission than DQW coupler for the TE111-type and TM110-type passband.

## Slide 6: HOM-damping studies
HOM-damping schemes
  Preliminary results for the two investigated configurations:
  2 Hook + 2 Probe couplers configuration provides a better damping of both monopole and dipole HOMs than the 2DQW couplers
  However, the trapped TM012 mode was not damped in the two configurations (modification of the end-cells is needed to enhance the coupling to the beam tube)
TM010
TM011
TM020
TM012
TE111
TM110
TM111
TE112
TM120
  Objective: extract the energy of the HOMs from the cavity.

## Slide 7: Conclusions
  Future perspectives:
  Optimization of the cavity end-cells to improve the coupling of the TM012 π-mode to the beam tubes
  Optimization of HOM couplers, and study of other HOM couplers (JLAB, TESLA)
  Thermal studies for HOM couplers (HOM power and dissipation)
  Eigenmode and wakefield analyses were carried-out in CST Studio Suite® to investigate on the HOM behavior of PERLE Cavity
  Potentially dangerous monopole and dipole HOMs were identified and classified until 2.4 GHz. A trapped monopole HOM was found at ~2.25 GHz
  HOM-damping scheme studies: 2 Hook + 2 Probe couplers configuration gives a better damping of both monopole and dipole HOMs than the 2DQW couplers

## Slide 8: Bibliography
  [1] D. Angal-Kalinin et al., PERLE, Powerful Energy Recovery Linac for Experiments, CDR, Journal of Physics G: Nuclear and Particle Physics, 45(6):065003, 2018.
  [2] W. Kaabi, PERLE: A High-Power Energy Recovery Facility at Orsay, February 2021.
  [3] F. Marhauser, PERLE Cavity Design and Results and First Thoughts on HOM-Couplers, PERLE HOM Coupler Meeting, October 2019, CERN.
  [4] T. Wangler, RF Linear Acceleratos, John Wiley & Sons, 2008.
  [5] CST Studio Suite manual, CST Studio, 2021.

## Slide 9: Thank you for your attention!