## Slide 1: Development of a 150MeV laser-plasma injector
Journées Accélérateurs ROSCOFF 2021
Drobniak Pierre
October 13th 2021

## Slide 2: 1 –Project
Laser Wake Field Acceleration (LWFA) [1]
[1] Malka, V., Thaury, C., Corde, S., Phuoc, K. T., & Rousse, A. (2013). Accélérateurs à plasma laser: principes et applications. Reflets de la physique, (33), 23-26.
Plasma cell (gas cell in our case)
Gas injection
e-
40 fs, 30TW, ~1.2J, 10 Hz
on target (from LaseriX platform)
Ionization injection assisted by density modulation
150-200 MeV
30 pC
10Hz
1 mm.mrad ΔE/E <5%
My PhD
The laboratory project
https://pallas.ijclab.in2p3.fr/
http://www.eupraxia-project.eu/
e- bunch
Laser pulse
Plasma wake
Plasma Cell design
high quality beam
Stability at 10 Hz
Participation to R&D Technical Design Report in preparatory phase on high-quality laser-plasma injector (LPI) for EUPRAXIA Horizon 2020 European project
Beam transport -> multi-stage
Prototyping Accelerator based on Laser-pLASma technology

## Slide 3: 2 – Optimization principle
[1] Audet et Al. (2018). Gas cell density characterization for laser wakefield acceleration. Nuclear Instruments and Methods in Physics Research Section A: Accelerators, Spectrometers, Detectors and Associated Equipment, 909, 383-386.
[2] Kononenko, et Al. (2016). 2D hydrodynamic simulations of a variable length gas target for density down-ramp injection of electrons into a laser wakefield accelerator. Nuclear Instruments and Methods in Physics Research Section A: Accelerators, Spectrometers, Detectors and Associated Equipment, 829, 125-129.
[3] Kirchen et Al. (2021). Optimal Beam Loading in a Laser-Plasma Accelerator. Physical review letters, 126(17), 174801. [4] Couperus, J. P., Pausch, R., Köhler, A., Zarini, O., Krämer, J. M., Garten, M., ... & Irman, A. (2017). Demonstration of a beam loaded nanocoulomb-class laser wakefield accelerator. Nature communications, 8(1), 1-7.
[5] Jalas et Al. (2021). Bayesian Optimization of a Laser-Plasma Accelerator. Physical review letters, 126(10), 104801.
Cell design
OpenFOAM-simulated electronic density
Experimental qualification on test bench
Theoretical profile and PIC simulated laser variation
Longitudinal distance
ne , -- CN2 [x1018 cm-3, %]
a0 , -- a0_vac
Energy [MeV]
Spectrum [pC/MeV]

## Slide 4: 3 –Setup of the gas cell test bench
Dichroic mirror for dopant localization
LaseriX input beam, 60mJ, 45fs, 10Hz
Wave front sensor
Diagnostic beam
Reconstruction of the absolute phase shift (Abel inversion)
Camera
Plasma induced phase shift in the diagnostic beam wave front
Plasma cell
delay line
+ spectral filter centred on N2 emission lines
Plasma
Pump beam
Reconstruction of the plasma density
[1]
[1] Plateau, G. R., Matlis, N. H., Geddes, C. G. R., Gonsalves, A. J., Shiraishi, S., Lin, C., ... & Leemans, W. P. (2010). Wavefront-sensor-based electron density measurements for laser-plasma accelerators. Review of Scientific Instruments, 81(3), 033108.

## Slide 5: 4 – First experimental results
Test cell 1
Max. pulse energy
30 µm
Sensitivity ~ 1017cm-3
1 developped in the frame of the ESCULAP project (N. Delerue, K. Wang, J. Jenzer et al. ), used as a test cell [1]
[1] Baynard, E. et al. Status report of the ESCULAP project at Orsay: External injection of low energy electrons in a Plasma. Nuclear Instruments and Methods in Physics Research Section A: Accelerators, Spectrometers, Detectors and Associated Equipment 909, 46–48 (2018).

## Slide 6: 5 – Next steps
SHORT TERM
1 – Implementation first prototype on test bench
2 – Plasma ignition and measurements (using a mixture)
3 – Optimization of gas density (and mixture)
4 – Characterization of dopant migration
LONG TERM
1 – Plasma cell lifetime
2 – Integration of the plasma cell on the beam line (~ late 2022)
-> first electron bunches!
3 – Characterization of the electron bunch
First prototype
laser
Zoom inside chamber 1 and chamber 2
He+N2
He

## Slide 7: Thank you
Many thanks to: Kevin CASSOU, Sophie KAZAMIAS, Bruno LUCAS, Viacheslav KUBYTSKYI, Yann PEINAUD, Moana PITTMAN, Elsa BAYNARD, Julien DEMAILLY, Alexandre GONNIN, Stéphane JENZER