## Slide 1: Cavités optiques et systèmes lasers pour l’interaction laser-faisceaux (dont ThomX)

## Slide 2: Compton interaction as a monochromatic source
laser (Eλ=hc/𝜆=1.2eV)
α
θ
e- beam
Advantage:
Quasi monochromaticity obtained by use of collimator
Price to pay  Flux reduction
Compton photon:

## Slide 3: A wide range of applications
MightyLaser
ELI-NP-GS
ThomX
Compton energy threshold for λlaser = 1µm, 0.5µm
Maximum Scattered photon energy [MeV]
electron energy [MeV]
Low energy: 10keV to 1 MeV
Radiography & Radiotherapy
Art history
Material science
Medium energy (1 to 100 MeV)
Nuclear fluorescence, GDR
Nuclear physics
Nuclear waste management
Medical isotopes production
High energy (>100 MeV)
Electron beam polarimetry
𝛾𝛾 collider
Secondary beam production (ex: polarized positrons)
ILC
Amplitude/Radiabeam
SuperKEKB
+ GammaFactory

## Slide 4: What ?

## Slide 5: Ex: ThomX optical system
High quality factor (finesse) optical cavity

## Slide 6: Technical challenges
Noise measurement
Optical beating RF technique
30as integrated time jitter
10kHz
Higher-order mode degenerescence:
Residual absorption in coatings
Residual losses by diffraction (surface roughness)
Mirrors provided by IP2I/LMA
Metrology requirement on phase noise:
Unique provider now refuses to produce this type of laser
Look for alternatives…
Currently no R&D laser available (pulsed laser)

## Slide 7: ThomX photocathode
Quadrupled Yb laser
Operated by V. SOSKOV  Retirement in 2022/2023

## Slide 8: Material
Mode-lock frequency combs at about 1031nm
  MENLO orange fibre 175MHz, old, difficult to use but not used anymore. Maintenance may be needed.
  OneFive 62MHz. Maintenance required. Could be used for our R&D if can be repaired.
  ThomX lasers: 33Mhz and 133MHz working (or currently under maintenance)
Two CW ultra-stable lasers, being used with ThomX and current projects
Two fibre amplifiers 10-30W (not in use these days, but expected to be in the coming months)
3 green alignment lasers, 1 HeNe
Fibre soldering machine (PM fibre)
Spin-coater (to clean mirrors)
Various optics at 1030nm (mostly in use), optics at 515nm (un-used) + some blanks
Two optical spectrometers, one autocorrelator, Wavefront sensors, polarimeter
Vacuum devices, dust meter
Optical modulators (acousto, electro), doubling crystals
RF phase noise meter, PID electronics (LaseLock)
Bat. 208, salle ISO7
Bat. 209, salle ISO7, loc. ISO5
Bat. 209/PLIC, salle « grise »

## Slide 9: HR
RH: Points de vigilence et besoins pour les années à venir:
Expertise clé asservissement numériques et analogiques dédiés aux cavités optiques de R. CHICHE
  Plus d’une décennie de savoir faire unique
  Pérennisation sur le très long terme nécessaire si IJCLab veut continuer à contribuer
  Idéalement: identification d’un jeune compétent volontaire à former en vue d’un remplacement à 10 ans
Savoir faire de (>10 ans) sur la conception mécanique de nos systèmes par Y. PEINAUD
Renforts nécessaires:
  BE méca: gestion des effets thermomécaniques, en support au travail des doctorants
  IE optique: permanent dédié pour le soutien aux nombreux projets et lien technique continu sur le long terme
  AI/IE elec. analogique: manque depuis le départ de D. JEHANNO, profil difficile à trouver…
Air-conditionning contract:
  Several past issues with DALKIA that di not maintain properly the system for one of the rooms. Apparently solved since a month.
Statuts Chercheurs/Enseignants-chercheurs**
F. ZOMER (PdU, HDR, 50% 25%)
K. DUPRAZ (MCF, 25%  25%)
D. NUTARELLI (MCF, 50%  50%)
A. MARTENS (CRCNS, HDR, 100%  80%)
Statuts Ingénieurs/Techniciens
R. CHICHE (IR elec, 80% 80%)
Y. PEINAUD (AI BE meca, 70%  70%***)
K. CASSOU (IR opt., 80%  0-5%)
V. SOSKOV (IR opt., 5-10%  RETRAITE 2022-23)
*: convention: moyenne années passées  attendu années à venir
**: % de la part totale des activités
***: en phase de conception/installation
+ 2 to 3 students

## Slide 10: Un travail d’équipe réalisé par des doctorants
Christian
Ronic
Kevin
Viktor
Pierre
Xing
Fabian
Huan
Titouan
Daniel
Eric
Kevin
Denis
Yann
Loïc
Themis
Cheikh
+ Manar
+ Frédéric
Daniele