## Slide 1: Status and Perspective
of the Energy Recovery Linac at Helmholtz Zentrum Berlin
12/10/21, A. Neumann
IJClab Accelerator Seminar
Today
online

## Slide 2: Outline of today’s presentation
Artist view of bERLinPro Energy Recovery Linac Project at Helmholtz-Zentrum Berlin in Berlin Adlershof
Introduction:
  Why do we build an ERL?
  Challenges for ERL design and operation
Achievements during the bERLinPro project phase
  Mishaps and problems during the project phase
  SRF Gun Cavity development and operation
  Design studies for the main Linac
  SRF Booster injector and high power coupler conditioning
  Status of the warm machine and technical installations
Outlook: What are we doing next, applications for bERLinPro
  Injector studies and UED driver
  Test facility for HEP ERL studies
bERLinPro: An ERL demonstrator project
outline

## Slide 3: Where is bERLinPro?
Location
TH2, TH1: Cleanrooms, SRF Teststands
SLH
BESSY II
MLS
bERLinPro
Fala-FEL Place
N
Where are we?
897.5 km
Orsay
Berlin

## Slide 4: Why bERLinPro, why ERLs?
High energy electron cooling of bunched proton/ion beams
(e.g. hadron cooling of Electron-Ion-Collider EIC by BNL/JLAB)
Ultra high luminosity electron – ion collider (EIC, LHeC)
(ERL serving as high intensity electron factory for electron hadron collisions at LHeC (7TeV p, 50 GeV e-), similar as former HERA )
Compact radiation sources
(FEL, inverse Compton sources, next generation lithography, THz facility)
and more …: UED by injector
Next generation multi-user light source
(e.g XFEL oscillators, multi-ID facility as former ARC-en-ciel or 4GLS)
Many applications bERLinPro would deliver important results or milestones for
From next generation Lightsource to many applications, e.g. HEP
Introduction
ERLs allow efficient operation at high average brightness/luminosity with Linac class beam quality
 Reduces ecological footprint of large scale science, especially when combining with higher TC SRF technology

## Slide 5: bERLinPro ERL after re-scoping in 2012
introduction
beam dump
6.5 MeV, 100 mA
= 650 kW
linac module
3 x 7 cell SRF cavities
44 MeV
modified Cornell booster
3 x 2 cell SRF cavities
4.5 MeV
srf-gun
1.4 cell SRF cavities
1.5-2.3 MeV, single SC solenoid,
merger
dogleg
test and diagnostic line
Recirculator
bERLinPro: A demonstration facility for ERL science and technology
New developments:
Beam dynamics and manipulation (merger, recirculator, study beam break-up)
SRF systems: Photo-injector, high power booster, HOM damped Linac
Electron source: High repetition laser system high QE cathode development
Control of beam losses and radiation protection
High power beam dump
High power CW RF
  Few 100 kW class klystrons  Power couplers!
  Some 10 kW solid state amplifier
Diagnostics, synchronization machine protection, beam loss monitoring
A stable Cryoplant
Parameter | bERLinPro
Beam energy recirculator (MeV) | 50
Beam current ERL mode (mA) | 100
Frequency RF and Laser (GHz) | 1.3
Normalized emittance (mm mrad) | 1 (< 0.6 in simulations)
Bunch length (ps) | < 2 (ERL mode), 100 fs @ 10 mA
Beam losses | << 10-5 @ 100 mA

## Slide 6: Challenges for the SRF systems
Introduction
SRF Gun:
Low emittance high brightness beam
Insertion of a thermally isolated high QE Cs-K-Sn cathode (particulate free)
Control of field emission to avoid dark current based losses and halo formation
High current, high beam power operation (HOM, FPCs)
High emission RF field  beam dynamics optimized shape
Avoid coupler kick based emittance dilution
Synchronization Laser  RF, precise RF control
2.3 MeV, 100 mA
High beam power
High beam current
Intermediate field levels 10 MV/m
Low coupler kicks
Zero-crossing operation
SRF booster cavity (Cornell)
+4.5 MeV (100mA)
Low beam power
High beam current
Strong higher order mode damping
Higher field levels 19 MV/m
Multi-pass beam
Precise field control and tuning
Main linac cavity
+45 MeV (2x 100 mA, recovered)
Compact machine: All vacuum parts need to be treated within ISO 4-5 environment

## Slide 7: Beam break-up in ERLs by main Linac
Introduction
1st
2nd
Multi-pass transverse beam breakup (BBU):
An injected beam receives an initial kick by a given dipole higher oder mode (HOM) or excites in first pass a dipole mode by its initial injection caused offset
Following beam is deflected by the dipole mode and receives more offset  stronger excitation of HOM if phase advance by optics allows positive feedback
Single mode BBU can be mitigated by proper setting of optics phase advance (while preserving recovery) or by RF feedback techniques within cavity or transverse optics manipulations
Multi-mode problem usually tackled by proper HOM damping techniques
Sum and product of transport matrix, HOM polarization
Recirculation time
Single cavity, single HOM case!
TM110 magnetic field
TM110 electric field
Cavity figure of merits: R/Q, w determined by shape
HOM damping

## Slide 8: No machine without beam optics!
Achievements
Parameters at LINAC exit | 
Energy / MeV | 50.1
Bunch length / ps | 4.65
Emittance x,y / µm | 0.58/0.41
Energy spread / keV | 254
Injector and recirculator optics design, magnet layout, collimators
Wanted vs. unwanted beam studies, dark current, halo formation,
Beam break-up studies and countermeasures
Orientation of injector cavities optimized to:
  Reduce coupler kick effects
  Limit back travelling dark current towards cathode
  Short pulse and low emittance modes
M. Abo-Bakr, M. McAteer, J. Völker
B. Kuske, M. Matveenko, et al.
Booster field
emission
Dark current losses along
injector

## Slide 9: Complete impedance analysis of the machine
Achievements
Impedance analysis, optimization and final loss factor calculation of the complete bERLinPro ERL
Redesign of collimators, bellows, diagnostic sections, etc..
Basis for placement of temperature sensors along vacuum chamber
Wake field calculations done up to 30 GHz
Results re-mapped to bERLinPro bunch pattern
Similar studies done for cavity string of Linac, Booster
See H.-W. Glock et al.,
IPAC 2015, Richmond, VA

## Slide 10: bERLinPro, a collection of experiences, successes and mishaps
Achievements
1st Gun cavity was built too “short”  shifted frequency and degraded RF performance  X-ray tomography
Build up of infrastructure and training of personnel was not accounted for  Damned for success
Number of personnel never fully matched requirements
2nd Gun got severely damaged by manufacturer at final treatment stage  Refurbishment program started
Building was delayed by some years before being ready for users
Booster power couplers needed remanufacturing of warm parts
Booster cavity helium tank required reworking
Redesign of Gun module required because of thermal short
BESSY VSR redirected large part of personnel to another project
Vacuum beamlines delayed by rewelding parts
Rust in de-ionized water cooling circuits required complete exchange
………….
The past, disaster or success?

## Slide 11: But progress was made: SRF photo-injector (2010-2012)
3.10-5
1.1.10-4
Arc deposited
lead BNL
Laser
Cleaning
0.1 mJ/mm²
Achievements
First full SC photo-injector with first beam, QE studies, laser cleaning, etc  Contributes to E-XFEL and PolFEL still considered, studied and improved at DESY
First beam from
Lead cathode 04/2011
Cavity 1
Cavity 2
Emittance studies, thermal emittance models of arc deposited lead cathodes

## Slide 12: SRF Photo-injector (Gun)
SRF photo-injector: From cradle to grave and resurrection
Time
2013
VTA
Manufacture
2014-2016
HZB
VTA/HTA
Test/Assembly
HTA
String test
12
HZB
Module assembly
Gunlab
String/Cold mass
2016
2017/2018
Commissioning
Cathode transfer
1st Beam
2018-2021
Decommissioning
Refurbish
Rebuild
Commissioning in 2022
2011-2012
HZB
Design
PC
bERLinPro
Fully in-house developed SRF photoinjector with strong partners
Achievements

## Slide 13: SRF Gun Cavity design
Overview: Injector Cavity 1
Achievements
2xCW modified TTF-III
Coupler: Qext 3.6.106
for up to Iavg=6 mA,
10 kW each
Study 2 coupler operation
106 mm beam tube:
Allows propagation of
lowest TM110 mode:
HOM studies
Blade tuner with
motor and 4x piezo tuner:
Microphonics compensation
3 pick-up antennas to measure HOM
polarization
0.4.l cell + full cell:
Optimized
emission phase
HZDR cathode
insert and choke
cell design:
Proven system
Cathode exchange
with HZDR
Stiffening ring:
Df/DP minimized
Chimney 22 cm²~35 W at 1.8 K
about Epeak=45 MV/m at Q0=3.5.109

## Slide 14: Cold String layout of bERLinPro SRF Gun
Achievements
SC solenoid
Twin CW-modified
TTF-III coupler up to 20 kW
x, y steerer
SiC HOM
absorber (Cornell)
Cathode tube with tuner (HZDR)
Gate valve
and transition
to 300K
Cavity+LHe vessel (HZB, JLab),
Cornell-type blade tuner,
2 layer magnetic shielding
Support
structure
*
*
*
80K
80K
4K
1.8K
4K
1.4xl/2 cells + Choke cell
*15-20% higher
found by beam
energy measurements

## Slide 15: Module layout
Achievements
80K helium
shield
2nd magnetic
shield
Holders and bellows for alignment
External Solenoid hexapod mover with feedthroughs
Cathode transfer system port
Beam
HGRP
4K cooling:
  Solenoid
  HOM load
  FPCs
4K filling line cavity
1.8 K JT line cavity
80K FPC and HOM
80 K shield and cathode
Both doors can be opened
Solenoid shielding:
Cryoperm around solenoid might saturate
Replaced by Nb disc between Solenoid and cavity outer shield, efficiency factor 5-8 to be published by J. Völker et al.
Modified: Issue with thermal short
Module layout of bERLinPro SRF Gun

## Slide 16: Transfer system and cathode carrier (HZDR modification)
Achievements
Module+transfer system
Transfer system behind module
Cathode cooler (80 K Helium) and Petrov filter holding the insert with tuner
Cathode insert with Plug
and transfer rod
3(4) thermal transitions
Plug: Ø 10 mm

## Slide 17: Operation of first 1.4 cell SRF Gun with cathode exchange mechanism
Achievements
First beam 12/2017
SRF Gun module
01/2018 Operation with high QE cathode failed,
as cathode plug dropped into Gun cavity by malfunction of holder mechanism 
QE map

## Slide 18: Development of high QE cathode and drive Laser
Achievements
doi:10.1103/PhysRevAccelBeams.21.113401
Last evidence of cathode being alive
Photocathode preparation and analysis laboratory up and running since 2015
- insight into growth process with material science studies in parallel
- achieved quantum efficiency of 16.8% at 515 nm (specs 1%)
- successful transfer from cathode lab to SRF gun
- demonstrated, that cooling of cathode to 120 K do not harm quantum efficiency (unlike prediction by other researchers!)
We were close to
operate this record cathode in Gunlab…….
And learned from our
fails…..
…cathode holder
heating and shock experiments

## Slide 19: Recent Achievements  Refurbish SRF Gun
Recent activities
1.1
1.0
Y. Tamashevich, et al. published SRF21
Both cavities were damaged: 1.0 Initial scratch after production  Dark current 1.1 got damaged at manufacturer
A repair and refurbishment program was set up between 06/2019 until 06/2021
Treatment by grinding, polishing, BCP and optimized HPR system, HF rinsing 
1.1: HPR lance scratch
1.1 After grinding and polishing
1.0: surface defects
Gun 1.0 is back on track
Gun 1.1 will be back-up
Gun 1.0

## Slide 20: Impressions of Gun cold string assembly
Recent activities
Petrov+cooler positioning
Determine cathode position
Concentricity check with dummy cathode
Completed cold string leak tight and evacuated, accomplished for Nikolaus!
Preassembled sub- components
Detailed, accurate preparation led to quick, but not imprecise assembly
Key was documentation of the past (2016) and a motivated and well working team
Thanks to: André, Michael, Henry, Jan, Frank and fast support from the workshop

## Slide 21: Cold String Role out and preparation for cold string test in HTA
Recent activities
Prior to module assembly, a full cold string test is the final acceptance test in HoBiCaT:
Test if Q0 and max. E-field is preserved after assembly
Did we activate any field emitters by improper handling?
Test of tuner system, coarse and piezo stacks
Characterization of parameters for LLRF control
HoBiCaT with support
Table for cold string
Cold String test assembly
Role out

## Slide 22: Linac studies
Achievements
Design was ready for production, study performed with company
HOM prototype fabricated and tested by JLab
Module was optimized for high level beam break-up current and to preserve beam quality, BBU study of full 3 cavity string
Optimization of interconnecting structures w.r.t. localized modes
Minimization of coupler kicks studied
T-Map of succesful HOM test
Tmax (50 W) = 64.9 C
Heating derived by HOM
simulations

## Slide 23: High power Booster module + couplers
Achievements
Beam power 450-500 kW, 220 kW/cavity with twin coupler arrangement
Thus 120 kW travelling wave supplied by one 250 kW klystron per FPC
Design needs to avoid coupler kicks and emittance dilution
HOM damping by beam tube absorbers
Cavities outperform specs
Coupler are being conditioned
HOM arrival this winter  all parts for cold string in house

## Slide 24: Recent Achievements  High Power Coupler Processing
Recent activities
Parameter | Required Gun 1: 6 mA | Required Gun 2: 100 mA | Values reached so far
Traveling wave | 7 kW | 110 kW | 60 kW CW 120 kW 10% Duty Cycle
Standing wave | 1.75 kW | 54 kW | 15 kW
3 out of 4 pairs conditioned, 4th pair in 2022

## Slide 25: Warm beamline, magnets, diagnostics, power supplies
Achievements
Budker Institute
of Nuclear Physics
All girders and magnets
Installed and
pre-aligned
Particulate-free
UHV vacuum system + 600 kW beam dump:
ISO 5
NEG coated
Under vacuum and waiting

## Slide 26: A glance at diagnostics and vacuum system
Achievements
Beamloss
diagnostics
Vacuum sectors
Beam
diagnostics
+ Control system EPICS, visualization and data archiving
Jupyter Notebooks for
Python based data analysis and measurement programs
18x screen stations
24x Striplines, of which 8 with Ion clearing
2x button ion clearing
6x current monitors (ICT)
5x collimators
2x Faraday cups
3x Beam dumps
2 segmented Faraday cups
1 transverse defl. Cavity
Option: 6x THz/Sync. Rad.

## Slide 27: RF and cryogenics installation status
Achievements
1.3 GHz CW 270 kW Klystron Second test in dummy load
600 kW FuG power supply
Made by CPI
3 Klystrons in house, 1 tested in SLH and at bERLinPro, currently in use for coupler conditioning
2 Klystrons will power Booster, 1 a high power gun at some point
15 kW solid state amplifiers for Linac Tcav and 1st Booster (zero-crossing)
N2 to cool L700
Waiting for final commissioning mainly cold compressor operation missing (1.8K)
Pics
courtesy
W. Anders
Booster+Gun coldbox

## Slide 28: Recent Achievements  Completion of Recirculator vacuum
Recent activities
Recirculator vacuum is closed since summer 2021, final survey of the machine within the building
We just need a Linac module and would be a real Energy Recovery Linac
Pics: Courtesy J. Völker

## Slide 29: View of the photo-cathode laser and its control
pulse train oscillator (50 MHz)
pulse stretcher,
1st pulse selector
1st preamplifier
2nd preamplifier
power amplifier
2nd pulse selector
pulse compressor,
IR VIS conversion
tunable pulse stretcher for „green“
~40 W green
control
synchronization
diagnostic
50 MHz Laser Channel
currently stand-alone operation (no control system, no master clock from accelerator infrastructure)
1.3 GHz Laser Channel
to be placed on free space beneath 50 MHz-setup, amplifier stages will partly be shared
still under development at MBI:
  A reliable solution for the pulse train oscillator has finally been found (main difficulty: tight space within optical cavity for 1.3 GHz rep. rate)
  next steps:
    adapt synchronization,
    test concept for enhanced efficiency in IR to green-light conversion
    adapting control
29
Courtesy
G. Klemz
Recent activities
Alignment beam in accelerator hall
Bunch spacing and current options:
50 MHz Laser:
  1-100 Hz macro-pulse:  Iavg = 77 pA – 7.7 µA
  CW 3.8 mA
1.3 GHz Laser:
  1 Hz – 1 kHz macro-pulse:  Iavg = 77 pA – 20 µA
  CW 100 mA
All this with 77 pC bunch charge, laser power set up for QE of 1 %

## Slide 30: bERLinPro, quo vadis?
outlook
New project heads?
Old project heads?
ARD
JEAN LOUIS THÉODORE GÉRICAULT - La Balsa de la Medusa (Museo del Louvre, 1818-19)
John Tenniel - Punch, 29. März 1890, “Der Lotse geht von Bord”
The project was completed in 2020
But only to continue as a research facility!
Let’s have anyway a glimpse into the future
bERLinPro?
HMS bERLinPro

## Slide 31: What is coming next?
From bERLinPro to SEALAB (SRF Electron Accelerator LABoratory)
outlook
So far bERLinPro was conceived solely as an energy-recovery linac test facility: 100 mA average current, 50 MeV, en<1 mm.mrad Now the scope was extended.
We want to open the machine up to internal and external applications:
  Completion of the injector and linac/dump lines: Commissioning Injector with beam (up to 5 mA, up to few 100 pC, up to 6.5 MeV)
  UED experiment  Aiming for shortest pulses, synchronization
  Offer the injector as a testbed to test and commission AI/machine learning techniques, digital twins, as long as Linac gap is open: Test area for (S)RF cavities, modules (e.g. MESA)
  Map the complete attainable injector phase space for many applications: From FEL, UED to HEP
  Testing of new diagnostics, acceleration concepts and controls
  Collaborate with external partners for a 100 mA compatible Linac module in most efficient design, e.g. fast reactive tuners, optional 4K operation of single cavity (ERL initiative for HEP)
SRF Gun
SRF Booster
FOMZ1ZAF at 12.69
UED Detector
FCUPZGAF
Aperture
FOMZ1MAF at 7.64
UED Target & Viewscreen
Solenoid
Ultrafast Electron
Diffraction modifications
FRT, courtesy N. Shipman CERN

## Slide 32: Acknowledgements
Fin
We would like to acknowledge:
J. Teichert, A. Arnold, P. Murcek, R. Rimmer, A. Burrill, F. Marhauser, S. Belomestnykh, E. Zaplatin, E. Kako, R. Eichhorn, J. Sekutowicz, P. Kneisel, G. Ciovati, A. Matheisen, B. van-der-Horst, M. Schmökel, W.A. Clemens, C. Dreyfuss, D. Forehand, T. Harris, R.B. Overton, L. Turlington, M. Schalwat, S. Lederer, V. Volkov, I. Will, MAC members
+many more
HZB bERLinPro Team & friends
former colleagues
Thanks for your attention!
Budker Institute of Nuclear Physics